## Slide 1
RRC (Radio Remote Control App for Motorola Solution Enterprise Division
RRC App makes a connection between a personal phone and Apex two-way public safety radio
used by public safety departments (Police departments, health departments, etc).
This app uses Bluetooth connection over a range of 10-20 feet
Most of the functionality of this app is limited at this time due to unviability of public safety radio
and propriety information. So, only few screens will show up from a UI flow’s point of view.
Source code can’t be provided due to the propriety information. Apk and flow of the application is provided
In this presentation

## Slide 2
General Understanding:
USB Samsung Driver (if one is using Galaxy Nexus phone). Please put “SAMSUNG” under Program files.
Android SDK with Eclipse and ADT plugin is needed to modify and build the application.
Install the RadioRemoteControl.apk in your phone. One can use adb_install.bat script to do just that.
Sometimes, pairing and connection between an Apex radio and a smart phone doesn’t happen. In that case, please clear the BT pairing from Apex radio. Please follow the instructions below:
i) Turn on the Apex radio
ii) Keep pressing “right arrow” button until one sees “BT” on the menu screen.
iii) Now, press the button right below where “BT” is written
iv) Keep pressing the “down arrow” button until one highlights the “Devices”
v) Now, press te button right below where “Clr” is written
vi) Now, press the button right below where “Yes” is written
vii) Power cycle the radio and then try again running the application
5) Once application builds in eclipse, one can find the apk under the following folder:
RadioRemoteControl  bin  RadioRemoteControl.apk
Organization of RRC Source Code
Bluetooth : RadioRemoteControl  src  com.motorola.rrc.bt (Java files)
DTAPI: RadioRemoteControl  src  com.motorola.rrc.dtapi (Java files)
UI: RadioRemoteControl  src  com.motorola.rrc.ui (Java files)
Logger file: RadioRemoteControl  src  com.motorola.rrc.nsc (Java files)
Layouts (screens) files: RadioRemoteControl  res  layout (XML files)
Images: RadioRemoteControl  res  drawable-hdpi
Strings: RadioRemoteControl  res  values  strings.xml
Styles: RadioRemoteControl  res  values  styles.xml (It has style for standard android Actionbar)
Menu: RadioRemoteControl  res  menu  activity_main_menu.xml, main_control_screen_menu.xml, menu_pair_to_new_radio.xml (these are the Actionbar Menu items xml files that are used in standard and splitactionbar menu)
AndroidManifest.xml: RadioRemoteControl  AndroidManifest.xml

## Slide 3
Launching the RRC App
LF Pairing
BT Connection Establishment
LF Pairing Time out
Connection Time out
Unpair during the time out
Unpair
Zone/Channel Display
DTAPI (CodePlug, RRCData)
Logger

## Slide 4
MainActivity.java
(activity_main.xml)
DTAPI Service Available
DTAPI is LF Paired
else
MainActivity.java
(activity_main.xml)
{Pair to New Radio Screen}
MainControlScreen.java
(activity_main_control_screen)
{Zone/Channel Main Screen}
AttemptingToConnect.java
(attempting_to_connect.xml)
{BT Establishment Screen}
Click on
Pair to New Radio
DTAPI is LF Paired
AttemptingLFPairing.java
(activity_display_message.xml)
{LF Pairing Instructions Screen}
1st Time
Successful
LF Pairing Timed Out
PairingTimedOut.java
(activity_pairing_timed_out.xml)
TRY AGAIN
Is BT Turned
ON??
NO
Pop UP Message
(AlertBox)
ALLOW??
YES
BTConnectionTimeout.java
(activity_bt_connection_timeout.xml)
NO
TRY AGAIN?
Unpair?
YES
MainActivity.java
(activity_main.xml)
{Pair to New Radio Screen}
Unpair
MainControlScreen.java
(activity_main_control_screen)
{Zone/Channel Main Screen}
Yes

## Slide 6
RCC App Icon
App Launch Screen
Pairing with Two-way Mobile Radio
Tap to try again

## Slide 7
Turn on Bluetooth
Main Channel/Zone Screen
Main Channel/Zone Screen

## Slide 8
Zone Selection Screen
Channel Selection Screen